## Slide 1: Aerospace Modeling Tutorial Lecture 2 – Basic Aerodynamics
Greg and Mario
February 2, 2015

## Slide 2: Our system dynamics:

## Slide 3: Our model

## Slide 4: Navier Stokes Equations

## Slide 5: Solving Navier Stokes - CFD
Computationally demanding
Not suitable for real time simulation
Not suitable for dynamic optimization

## Slide 6: How to simplify things?

## Slide 7: Thin airfoil theory
Assumptions:
2-dimensional flow
Inviscid flow
Incompressible flow
Solve simplified NS (just Laplace’s equation) with flow tangency condition

## Slide 8: Thin airfoil theory
Results:
(Lift)
Advantages:
Easy to compute
Fits well to data
Drawbacks:
Predicts 0 drag
Real wings aren’t 2-dimensional

## Slide 9: xfoil
viscous solution in the boundary layer
Inviscid outside
gives parasitic drag
still 2d

## Slide 10: Prandtl lifting line theory
Still inviscid, incompressible
Model flow field as a sum of horseshoe vortices
Solve for circulation of each 2-d section
Still need to account for wing-tail interaction
Ignores spanwise viscous flow

## Slide 11: Vortex lattice
Model the wing as a panel of ring vortices
Can handle arbitrary shapes
Disadvantage: intrinsically computational, no handy formulas

## Slide 12: AVL – Athena Vortex Lattice (Mark Drela)
popular code, includes parasitic drag
Inputs: geometry, alpha/beta/airspeed
Outputs: force/moment vectors + derivatives w.r.t. omega
Strategy: sweep alpha/beta, fit curves for all coefficients

## Slide 13: Our model

## Slide 14: Homework 1: 2-dimensional model
Mass 2
Aspect ratio 10
Sref 0.5
Gravity 9.8
State:
Control input: α
Starting from [0,-10,10,0], fly as far as possible in 10 seconds, in the x direction
Starting from the same place, fly as long as possible (maximum time)
Altitude must always be positive!!

## Slide 15: Homework 2 (optional): 3 dimensional model
Implement the full aerodynamic model, using coefficients from https://github.com/ghorn/rawesome/blob/master/rawe/models/betty_conf.py
(There is also a reference model there)
R(0) = eye(3)
p(0) = [0,0,0]
v(0) = [15, 0, 0]
ω(0) = [1, 0, 0]
Do something like, R(5.0)=eye(3), w(5.0) = [0,0,0], vy(5.0) = 0, minimize u^2
Probably best to simulate first to validate model